## Slide 1: Computer Organization and Architecture William Stallings 8th Edition
Chapter 1 Introduction

## Slide 2: Architecture & Organization
Architecture is those attributes visible to the programmer, or those attributes that have a direct impact on the logical execution of a program.
      Instruction set, number of bits used for data representation, I/O mechanisms, addressing techniques.
Organization is how features are implemented, or the operational units and their interconnections that realize the architecture specification.
      - Control signals, interfaces, memory technology.

## Slide 3: Forces on Computer Architecture
Computer
Architecture
Technology
Programming
Languages
Operating
Systems
History
Applications

## Slide 4: Architecture & Organization
- All Intel x86 family share the same basic architecture.
- The IBM System/370 family share the same basic architecture.
- Organization differs between different versions.
Computer Architecture =
Instruction Set Architecture +
Machine Organization

## Slide 5: Architecture & Organization
However, because a computer organization must be designed to implement a particular architecture specification, a through treatment of organization requires a detailed examination of architecture as well.
instruction set
software
hardware

## Slide 6: Structure & Function
Structure is the way in which components relate to each other.
The Five Classic Components of a Computer
  Input (mouse, keyboard, …)
  Output (display, printer, …)
  Memory
    main (DRAM), cache (SRAM)
    secondary (disk,
    CD, DVD, …)
  Datapath
  Control
Function is the operation of individual components as part of the structure.
Processor
(CPU)

## Slide 7: The Five Classic Components of a Computer

## Slide 8: Function
All computer functions are:
  Data processing
  Data storage
  Data movement
  Control

## Slide 9: Functional View

## Slide 10: Operations (a) Data movement
The computer must be able to move data between itself and the outside world.

## Slide 11: Operations (a) Data movement
When data are received from or delivered to a device that is directly connected to the computer, the process is known as input–output (I/O), and the device is referred to as a peripheral.
When data are moved over longer distances, to or from a remote device, the process is known as data communications.

## Slide 12: Operations (b) Storage
The computer must temporarily store at least those pieces of data that are being worked on at any given moment.

## Slide 13: Operation (c) Processing from/to storage

## Slide 14: Operation (d) Processing from storage to I/O
The data may take a wide variety of forms, and the range of processing requirements is broad.
Files of data are stored on the computer for subsequent retrieval and update.

## Slide 15: Control the three functions
Finally, there must be control of these three functions.
Ultimately, this control is exercised by the individual(s) who provides the computer with instructions.
Within the computer, a control unit manages the computer’s resources and orchestrates the performance of its functional parts in response to those instructions.

## Slide 16: Structure
This figure is the simplest possible depiction of a computer.

## Slide 17: Structure
The computer interacts in some fashion with its external environment.
In general, all of its linkages to the external environment can be classified as peripheral devices or communication lines.

## Slide 18: Structure - Top Level
Computer
Main
Memory
Input
Output
Systems
Interconnection
Peripherals
Communication
lines
Central
Processing
Unit
Computer

## Slide 19: Structure - The CPU
Computer
Arithmetic
and
Login Unit
Control
Unit
Internal CPU
Interconnection
(Bus)
Registers
CPU
I/O
Memory
System
Bus
CPU

## Slide 20: Structure - The Control Unit
CPU
Control
Memory
Control Unit
Registers and
Decoders
Sequencing
Login
Control
Unit
ALU
Registers
Internal
Bus
Control Unit

## Slide 21: Main structural components
Central processing unit (CPU) controls the operation of the computer and performs its data processing functions; often simply referred to as processor.
Main memory stores data.
I/O moves data between the computer and its external environment.
System interconnection some mechanism that provides for communication among CPU, main memory, and I/O e.g. system bus.

## Slide 22: Main structural components
CPU is the most interesting and the most complex component.
Its major structural components are as follows:
  Control unit (CU) controls the operation of the CPU and the computer.
  Arithmetic and logic unit (ALU) performs the computer’s data processing functions.
  Registers provides storage internal to the CPU
  CPU interconnection some mechanism that provides for communication among the control unit, ALU, and registers.

## Slide 23: Outline of the Course - CS323
We will cover the following chapters of our course:
  Computer Evolution and Performance
  A top-level view of computer function and interconnection
  Cache memory
  Internal Memory
  External Memory
  Input/Output
  Operating Systems Support
  Computer Arithmetic

## Slide 24: Internet Resources - Web site for book
http://WilliamStallings.com/COA/COA7e.html
  links to sites of interest
  links to sites for courses that use the book
  errata list for book
  information on other books by W. Stallings
http://WilliamStallings.com/StudentSupport.html
  Math
  How-to
  Research resources
  Misc

## Slide 25: Internet Resources - Web sites to look for
WWW Computer Architecture Home Page.
CPU Info Center.
Processor Emporium.
ACM Special Interest Group on Computer Architecture.
IEEE Technical Committee on Computer Architecture.
Intel Technology Journal.
Manufacturer’s sites:
  Intel, IBM, etc.

## Slide 26: Internet Resources - Usenet News Groups
comp.arch
comp.arch.arithmetic
comp.arch.storage
comp.parallel
Next task:
Computer History
http://www.computerhistory.org/timeline